## Slide 1: MDP Project Overview
Jan, 2017
Yong

## Slide 2: Content
Project Description
Sample 1D Cooling System Results for Milestone 1
Sample 3D CFD Waterjacket Results for Milestone 1

## Slide 3: Project Description
Topic: Full Vehicle Cooling System Model Development
Description: Develop a complete 1D/3D vehicle cooling system model for Isuzu’s Model Based Engine Development. This model can be used for sizing coolant pump and radiator, along with heat rejection prediction for the engine cylinder and thermal analysis of full vehicle cooling system.
2017 Planning:
Jan |  | Mar |  | Apr |  | Jun |  | Aug | Sept | Oct | Nov | Dec
Milestone 1 |  |  | Milestone 2 + Extra Topics |  |  |  |  | Milestone 3 |  |  |  | Wrap up -Next Step
Group: GT power 3; Converge 2; Data Analysis and post-processing: 1

## Slide 4: Milestones
Milestone one :
1D steady sate isothermal GT under-hood cooling system, with fluid dynamics coming from:
1) Cylinder head water-jacket isothermal CFD simulation.
2) Use GEM3D for creating discretized model for geometry with bends or simple splits.
Target: This 1D cooling system can be used for pump sizing, radiator sizing and investigation of cooling system design.

## Slide 5: Milestones
Milestone two:
Upgrade the 1D cooling system model from isothermal steady sate to thermal steady sate by Using GT tool COOL3D thermal cooling modules.
Target: Develop a steady sate model capable of basic thermal prediction for the vehicle cooling system.

## Slide 6: Milestones
Transient Detailed Engine Thermal Coolant System. Develop fully thermal, detailed 1D GT model for the engine.
Milestones:
1. Build detailed engine cooling model with functionality of transient thermal mapping.
2. Couple the engine cooling system 1D model with the engine GT 1D model (Isuzu will provide the engine GT 1D model as black box with necessary outputs)
3. Implement Phase II detailed transient thermal engine model into Phase I full vehicle cooling system.
Target: Provide Transient Engine Heat Rejection Prediction for certain duty cycles.

## Slide 7: Extra Topics
Transform the 1D steady state GT full vehicle cooling simulation into transient thermal simulation.
Investigate possible solutions for other components as well: such as TaiTherm for cabin cooling, detailed model for CAC cooling, radiator etc.